## Slide 1: Nhat (Nick) Pham
Lecture 3: “ROS, Positioning, and Navigation”
(With grateful thanks to Andrew Markham and Johan Wahlstrom)
https://www.wired.com/story/amazon-warehouse-robots/

## Slide 2: ROS (Robot Operating System)
Notes: Ok, so let’s start with ROS, or, to give it its full name, Robot Operating System.

## Slide 3: What is ROS?
Notes: Ok, so let’s start with ROS, or, to give it its full name, Robot Operating System.

## Slide 4: ROS
“Robot Operating System (ROS or ros) is robotics middleware (i.e. collection of software frameworks for robot software development). Although ROS is not an operating system, it provides services designed for a heterogeneous computer cluster such as hardware abstraction, low-level device control, implementation of commonly used functionality, message-passing between processes, and package management.”
--Wikipedia
Notes: So what is ROS? Well, despite its name, it’s not actually an operating system so much as it’s a collection of software frameworks for robot software development. And it’s basically there to give you a platform of existing work to build on, so that you don’t have to spend lots of time creating common software components from scratch for each robotics project you undertake.
So for example, it provides lots of services designed for a heterogeneous computer cluster, such as hardware abstraction, low-level device control, implementations of common functions, inter-process message passing, and package management.

## Slide 5: ROS Definitions
Nodes: A process that performs computation or simply provides information to other nodes.
Topics: Nodes can publish information to a topic and every node that subscribes to that topic will receive the same information.
Services: Some nodes might need their data to be processed by other nodes (think of HTTP request) and this is done through services.
Parameter Server: Nodes use this server to store and retrieve parameters at runtime.
Master: One node to rule them all. ROS Master is a special node that keeps tabs on all topics, services and nodes that are available on the ROS Network. Communication between nodes are direct, but ROS Master tells each node useful information like IP, etc...
Notes: So in practice, ROS is effectively an ecosystem designed to make developing robotics applications easier and less painful. And like any ecosystem, it has its own terminology and idioms that you need to know about before you can really understand how it works. So let’s start by taking a look at a few basic ROS concepts.
So perhaps the most basic of ROS concepts is that of a node. And this is essentially just a ROS-based process that performs computation or provides information to other nodes. And note that in practice, ROS manages a network, and a ROS node can be running anywhere on the ROS network, either locally or on some other device.
So in order to facilitate the sharing of information between nodes, ROS introduces the concept of a topic. And this is essentially just a named intermediary between a node that wants to publish some information, and other nodes that want to subscribe to it. So for example, a node running on a robot might want to publish the trajectory of the robot as it moves around the scene, and a node running on a PC elsewhere on the ROS network might want to subscribe to this information and draw the trajectory on a screen for debugging purposes. Note that multiple nodes can subscribe to the same topic, in which case they will all receive identical copies of the information that has been published. Less commonly, multiple nodes can also publish to the same topic.
ROS also allows a node to act as a service. And a service is basically just a ROS node that exposes an interface and then processes requests made of it by other nodes.
Yet another ROS concept is that of a parameter server, which is basically just a place to store configuration parameters that can be accessed by nodes across the ROS network.
Finally, the entire ROS network is managed by a node known as the master node, which is basically a special node that keeps tabs on all topics, services and nodes that are available. Note that this node doesn’t get in the way of communications between other nodes, in that once they have found each other, they can communicate directly in a peer-to-peer way. But what it does do is make sure that they can find each other in the first place.

## Slide 6: ROS Definitions
Nodes talk to each other through messages. There are standard messages, but you can create your own.
A ROS package will contain the necessary messages, nodes and service definitions to complete a specific task.
You can develop your nodes in C++, Python and Lisp. MATLAB now contains a ROS Toolbox which allows you to interact with the whole ROS interface. A bit slow to be honest.
Source: http://wiki.ros.org/navigation
Notes: Ok, so ROS nodes in a network talk to each other through messages, and these can either be some of the standard messages, or custom messages that you create yourself.
And a set of messages, nodes and service definitions can be bundled together into a ROS package that is designed to complete a specific task.
From a development perspective, there are a number of languages in which you can develop ROS nodes, including C++, Python, Lisp and even MATLAB, although the latter is honestly a bit slow.

## Slide 7: ROS Communication
Master node
Node 1
*Provides Service A
*Listens to Topic B
Node 2
*Provides Topic B
Node 4
*Requests Service C
Node 3
*Provides Service C
Notes: Ok, so now let’s have a look at an example ROS network to aid us in understanding how the nodes communicate, and what role the master node plays in that process.
So in our example network, there are five nodes. Node 1 provides Service A and listens to Topic B, Node 2 provides Topic B, Node 3 provides Service C, Node 4 requests Service C, and the Master node coordinates all of the other nodes.

## Slide 8: ROS Communication
Master node
Node 1
*Provides Service A
*Listens to Topic B
Node 2
*Provides Topic B
Node 4
*Requests Service C
Node 3
*Provides Service C
Node 1
*Provides Service A
*Listens to Topic B
Node 2
*Provides Topic B
Node 3
*Provides Service C
Node 4
*Requests Service C
Notes: So how does the Master node do this? Well, for starters, it maintains a record of all of the other nodes in the network so that it can share this information with interested parties.

## Slide 9: ROS Communication
Master node
Node 1
*Provides Service A
*Listens to Topic B
Node 2
*Provides Topic B
Node 4
*Requests Service C
Node 3
*Provides Service C
Node 1
*Provides Service A
*Listens to Topic B
Node 2
*Provides Topic B
Node 3
*Provides Service C
Node 4
*Requests Service C
Topic B?
Notes: So for example, if Node 1 wants to listen to Topic B, it can first ask the Master node for the node that publishes Topic B.

## Slide 10: ROS Communication
Master node
Node 1
*Provides Service A
*Listens to Topic B
Node 2
*Provides Topic B
Node 4
*Requests Service C
Node 3
*Provides Service C
Node 1
*Provides Service A
*Listens to Topic B
Node 2
*Provides Topic B
Node 3
*Provides Service C
Node 4
*Requests Service C
Node 2
Notes: And in this case, that’s Node 2, so that’s what the Master node will tell Node 1.

## Slide 11: ROS Communication
Master node
Node 1
*Provides Service A
*Listens to Topic B
Node 2
*Provides Topic B
Node 4
*Requests Service C
Node 3
*Provides Service C
Node 1
*Provides Service A
*Listens to Topic B
Node 2
*Provides Topic B
Node 3
*Provides Service C
Node 4
*Requests Service C
Notes: And then once it’s received this information, Node 1 is able to communicate with Node 2 directly, without any further help from the Master node.

## Slide 12: ROS - Typical Scenario
www.clearpathrobotics.com
Notes: Ok, so now let’s consider a scenario in which you have a single sensor that collects data, and you want to process this data and visualise the results.
So how many nodes do you think are needed here, remembering that every node should perform a single task? Where would you put the Master node? Will the sensor node be publishing or should it be a service? And how many topics are needed?
Well, the number of nodes is likely to be at least four, since you’d expect there to be a Sensor node, a Computation node, a Visualization node and a Master node. And you’d probably put the Master node on the desktop, since if you want to add other devices to the network later, then they’re quite likely to be connected to the desktop, and it makes sense in that situation for the Master node to be on a machine that’s somewhere in the middle of the network, rather than on its periphery. And if the sensor is yielding a continuous stream of data, then you’d probably want the Sensor node to be publishing that, rather than only yielding individual datums on request, since multiple consumers can then access the same data in parallel, rather than each getting a datum from a different point in time. And in terms of topics, you’d expect there to be at least one for the raw sensor data and another for the processed sensor data.

## Slide 13: ROS - Typical Scenario
www.clearpathrobotics.com
Notes: So that’s all well and good, but what if you have communication issues between the Sensor node and the rest of the network?
Well, in that case, there are various options, from trying to fix the underlying problem, to buffering data at the Sensor node and transmitting it later, to simply discarding the data and not worrying too much about it. And the right choice will generally be application-dependent.

## Slide 14: ROS – Available libraries
Standard Message Definitions
Robot Geometry Library
Robot Description Language
Diagnostics
Pose Estimation
Localization
Mapping
Navigation
Notes: So here are a few useful ROS concepts that you might want to look into a little bit more on your own.
So we already mentioned standard vs. custom messages. The Robot Geometry Library contains packages for common geometric calculations, including the ROS transform library tf, as well as bindings for the Bullet physics engine. The Robot Description Language offers a unified way of describing the geometry of a robot: see also URDF. The ROS diagnostics system is used for troubleshooting. And ROS also has various packages for pose estimation, localization, mapping and navigation, and it’s helpful to get at least somewhat familiar with those.

## Slide 15: ROS
https://www.cse.sc.edu/~jokane/agitr/
Notes: Incidentally, there’s a good book on ROS available for free, as shown in this slide, so if you want more information on anything we’ve talked about so far, that’s a useful resource.

## Slide 16: Challenging Scenarios: Firefighter
Notes: Ok, so now let’s move on from ROS, and talk a little bit about a challenging scenario, that of helping firefighters navigate around a building in an emergency.
And so here are some photos from when previous members of our group went to see a fire crew, so as to better understand the context of the problem.

## Slide 17: Challenging Scenarios: Firefighter
Notes: And this is them trying on some firefighting gear to allow them to better understand what things are like from a firefighter’s perspective.

## Slide 18: Challenging Scenarios: Firefighter
Firefighter positioning requires navigation systems that are
  Low-cost
  Independent of
    pre-deployed infrastructure
    fingerprinting databases
    environmental conditions such as visibility
Notes: Ok, so for determining the positions of firefighters in a building, we need navigation systems that
Are low-cost, since fire departments don’t have infinite money,
Are independent of pre-deployed infrastructure and fingerprinting databases, since these won’t generally be available for a particular building in an emergency, and
Are independent of the environmental conditions in the building, so for example don’t depend on the visibility being good when it might very well not be.
And unfortunately, this immediately rules out things like WiFi localisation based on pre-deployed access points, as well as things like visual localisation based on a colour camera, since the visibility may be poor.
So what can we use?

## Slide 19: Inertial Navigation (heads-up, heavy maths ahead!)
Notes: Well, one option might be inertial navigation based on an inertial measurement unit, or IMU.

## Slide 20: Inertial Sensors
Sensor​ | Measured quantity​ | Unit​
Accelerometer​ | Specific force​ | meter/second^2​
Gyroscope​ | Angular velocity​ | degree/second​
IMU = inertial measurement unit (typically a three-axis accelerometer and a three-axis gyroscope)
Notes: So an IMU is typically a combination of two different types of sensor, namely a three-axis accelerometer and a three-axis gyroscope. The accelerometer measures specific force (essentially the acceleration of the object it’s attached to minus gravity), whilst the gyroscope measures the angular velocity of the object. And you can use an IMU to obtain estimates of both the orientation of an object (from the gyroscope) and its position (by double-integrating the acceleration estimated by the accelerometer). Of course, the position estimated in this way is likely to drift quite a lot over time, so it’s common to look for ways to mitigate that.

## Slide 21: Inertial Sensors (Example demos)
Notes: So an IMU is typically a combination of two different types of sensor, namely a three-axis accelerometer and a three-axis gyroscope. The accelerometer measures specific force (essentially the acceleration of the object it’s attached to minus gravity), whilst the gyroscope measures the angular velocity of the object. And you can use an IMU to obtain estimates of both the orientation of an object (from the gyroscope) and its position (by double-integrating the acceleration estimated by the accelerometer). Of course, the position estimated in this way is likely to drift quite a lot over time, so it’s common to look for ways to mitigate that.

## Slide 22: Navigation using Foot-mounted Inertial Sensors
Not dependent on environmental conditions
Does not require external infrastructure
Low-cost technology
See also:
Pedestrian Tracking with Shoe-Mounted Inertial Sensors [Foxlin 2005]
Fifteen Years of Progress at Zero Velocity: A Review [Wahlström and Skog, 2021]
Notes: And so one interesting technology that tries to achieve this is navigation using foot-mounted inertial sensors. And there are several benefits of this technology:
First, inertial sensors aren’t dependent on the environmental conditions, and so this gives this approach a big advantage over something like visual odometry, which always requires visibility.
Second, the technology doesn’t require any external infrastructure, so you can start recording data anywhere and immediately get a positioning solution.
And finally, it is a low-cost technology, so for example, the mass-produced inertial sensors that are found in smartphones cost the manufacturer less than one pound each to make.
And so this technology can be used for any type of pedestrian navigation or motion analysis, such as firefighter positioning, military applications, or even biomedical applications, for example in the early detection of Alzheimer’s when you are looking for abnormal gait patterns that are associated with the disease.

## Slide 23: Navigation using Foot-mounted Inertial Sensors
I am here!
Notes: And so here’s what the inertial sensor looks like when one of the firefighters wears it on his foot.

## Slide 24: State-space Model
The navigation equations
The zero-velocity updates
: Navigation state
: Navigation equations
: Inertial measurements
: Inertial sensor errors
: Zero-velocity model
: Zero-velocity model errors
Solve the state-space model using some nonlinear filter or smoother, e.g., an extended Kalman filter.
Key observation: when a person’s walking, their feet alternate between a stationary stance phase and a moving stride phase, each lasting about 0.5 seconds.
Notes: Ok, so the problem of navigating using foot-mounted inertial sensors can be formulated using the state-space model shown in this slide.
And this formulation is based on the key observation that when a person’s walking, their feet alternate between a stationary stance phase and a moving stride phase, each lasting about 0.5 seconds. And if you can detect the stationary phases, you can use the fact that the velocity must be zero at that point to correct the velocity error after each stride, which reduces the growth in position error from cubic in time to linear in the number of steps. And so this was originally noted in the 2005 paper by Foxlin that I mentioned a couple of slides back.
So then the formulation itself consists of two sets of equations, namely the navigation equations and the zero-velocity updates, as shown in the slide. And so the navigation equations basically express how you update the navigation state, i.e. things like the position, velocity and orientation of the foot, from one time step to the next. So in other words, how you compute the navigation state at time k+1 from the navigation state, inertial measurements and modelled inertial sensor errors at time k. And the zero-velocity updates basically allow you to express that the velocity at a time step k is zero.
And so this state-space model can then be solved using some nonlinear filter or smoother, such as an extended Kalman filter. And if you want the gory details of that, I encourage you to take a look through the Foxlin paper, as it goes over it all in much more detail than we’re going to have time to do here.

## Slide 25: Navigation Equations
: Position
v : Velocity
C : Orientation (matrix)
: Sampling interval
: Accelerometer measurements
: Gyroscope measurements
: Gravity vector
: Identity matrix
: Skew symmetric matrix
Notes: Ok, so here are the details of the navigation equations mentioned on the previous slide. And these basically say the following things:
First, if you want to estimate the position at time k+1 from the position at time k, then you can simply add the velocity at time k multiplied by the length of the time step to it. And so this is just a classic forward Euler approach.
Second, if you want to estimate the orientation at time k+1 from the orientation at time k, then you can simply multiply the latter by , which is the result of adding a matrix representing the change in orientation over the time step, as measured by the gyroscope, to the identity. And that makes intuitive sense, because if there’s no change in orientation, then the gyroscope measurements will be zero and you’ll just end up multiplying Ck by the identity.
Third, if you want to estimate the velocity at time k+1 from the velocity at time k, then you can simply add the acceleration at time k multiplied by the length of the time step to it. And to calculate the acceleration, you multiply the estimated orientation at time k by the accelerometer measurements, and then add in the gravity vector. So again, that makes intuitive sense, because to interpret the measurements from the accelerometer, you need to know what orientation it’s at, and then you always need to take gravity into account as well after the fact.
Ok, so here are the details of the navigation equations mentioned on the previous slide. And these basically say the following things:
First, if you want to estimate the position at time k+1 from the position at time k, then you can simply add the velocity at time k multiplied by the length of the time step to it. And so this is just a classic forward Euler approach.
Second, if you want to estimate the orientation at time k+1 from the orientation at time k, then you can simply multiply the latter by 𝐼_3+Δ𝑡〖[𝜔]〗^×, which is the result of adding a matrix representing the change in orientation over the time step, as measured by the gyroscope, to the identity. And that makes intuitive sense, because if there’s no change in orientation, then the gyroscope measurements will be zero and you’ll just end up multiplying Ck by the identity.
Third, if you want to estimate the velocity at time k+1 from the velocity at time k, then you can simply add the acceleration at time k multiplied by the length of the time step to it. And to calculate the acceleration, you multiply the estimated orientation at time k by the accelerometer measurements, and then add in the gravity vector. So again, that makes intuitive sense, because to interpret the measurements from the accelerometer, you need to know what orientation it’s at, and then you always need to take gravity into account as well after the fact.

## Slide 26: Zero-velocity-aided Inertial Navigation
Navigation equations
Navigation estimate
at time k + 1
Inertial measurements
Navigation estimate
at time k
Zero-velocity detector
Information
fusion
Navigation estimate
at time k + 1
Zero-velocity
instances
Notes: Ok, so then here is a process diagram describing how a zero-velocity-aided inertial navigation system works at each sampling instance. So in other words, if we sample the inertial sensors at 100 Hz, we are also going to go through this whole process at 100 Hz.
So inertial navigation is iterative, and so at each iteration we’re going to take the navigation estimates at time k and produce navigation estimates at time k+1, the next sampling instance. And we do this by feeding the current navigation estimates and the current inertial measurements into the navigation equations shown on the previous slide, which ultimately derive from the underlying physics.
And then in addition to this, we’re also going to feed the inertial measurements to a zero-velocity detector that aims to detect when the foot is stationary. The zero-velocity instances and the navigation estimates will then be fused to improve the accuracy of the navigation estimates.

## Slide 27: Zero-velocity Detection
Compute likelihood ratio:
The foot is stationary
The foot is moving
E.g., (1) Angular Rate Energy Detector (ARED)
(2) Stance Hypothesis Optimal Estimation (SHOE) Detector
Wagstaff, Brandon, Valentin Peretroukhin, and Jonathan Kelly. "Robust data-driven zero-velocity detection for foot-mounted inertial navigation." IEEE Sensors Journal 20.2 (2019): 957-967.
Notes: Ok, so now let’s look a bit closer at the zero-velocity detector, which aims to detect when the foot is stationary.
And so the established method to do this is to compute a likelihood ratio, as shown in the slide, and when this likelihood ratio is above a specific threshold, the foot is assumed to be stationary. And in the equation, H1 denotes the hypothesis that the foot is stationary, and H0 denotes the hypothesis that it’s moving.
So that’s all well and good, but unfortunately it’s not obvious how to set the threshold gamma. And in practice, the optimal threshold tends to depend on a range of factors, including how fast you walk, exactly how the sensor is attached, the sampling rate, and so on. And clearly some of these can also change over time. So what can we do about this?

## Slide 28: Adaptive Thresholding
We show that
where
is the prior probability that the foot is stationary
is a loss factor, dependent on the risk of a missed
detection and a false alarm
Set by modeling and .
Wahlström, Johan, et al. "Zero-velocity detection—A Bayesian approach to adaptive thresholding." IEEE Sensors Letters 3.6 (2019): 1-4.
E.g., (1) prior probability
(2) Loss factor,
α and θ are design parameters, and tk is the time since the last zero-velocity instance.
where β1 and β2 are design parameters. For ξk to be a reliable measure of how close the system is to have zero velocity.
Notes: Well, the obvious approach is to vary the threshold over time, a technique known as adaptive thresholding.
And so it turns out that a principled way to do that is to reformulate the detection problem in a Bayesian setting, and to set gamma in terms of a time-varying prior probability p(H1) that the foot is stationary, and a loss factor eta that depends on the risk of a missed detection vs. that of a false alarm. So here a missed detection means that a step will be missed, whereas a false alarm will mean that a step gets detected when it shouldn’t have been.
So we’re not going to go into too much detail about that here, but you might want to take a look at the Wahlström and Skog survey paper if you’re interested.

## Slide 29: Performance Evaluation
After walking along a closed-loop trajectory with an approximate length of 84 meter:
Notes: So in terms of the performance difference that an adaptive threshold can make, here’s a graph showing the RMSEs for different fixed thresholds in comparison to an adaptive threshold after walking along a closed-loop trajectory with an approximate length of 84 metres. And you can see that even the best fixed threshold yields a much worse RMSE than the adaptive one, so it really is beneficial to adapt the threshold over time.

## Slide 30: Zero-velocity-aided Inertial Navigation
With zero-velocity updates
Without zero-velocity updates
Notes: Ok, so here’s a side-by-side comparison of foot-mounted inertial navigation with and without zero-velocity updates. And you can see that without the zero-velocity updates, the position estimates can be seen to diverge rather quickly, so this shows the necessity of using the updates.

## Slide 31: Position Error Growth
time
Position error
With zero-velocity updates: Linear position error growth.
Navigation | Navigation time
Stand-alone inertial navigation | A few seconds
Zero-velocity-aided inertial navigation | Several minutes
Without zero-velocity updates: Cubic position error growth.
Notes: Ok, so that was just an example, but we can also plot the growths in the position error with and without the zero-velocity updates, as shown in this slide.
And so without the zero-velocity updates, in other words if we just repeatedly use the navigation equations, we will have cubic error growth. This is because the error primarily stems from gyroscope errors, which are integrated three times. A cubic error growth means that when increasing the navigation time by a factor of two, the position error grows by a factor of eight. And so that’s not so good.
By contrast, with the zero-velocity updates enabled, the velocity errors are repeatedly set to zero. And since velocity is only one integration from position, zero-velocity-aided inertial navigation has linear position error growth.
And so in practice this might not sound like much, but it’s the difference between useful and useless odometry. Without zero-velocity updates, you can only navigate for a few seconds, assuming we are using low-cost sensors. However, with zero-velocity updates, we can typically compute useful navigation estimates for at least a couple of minutes without the use of any other information source.

## Slide 32: FootSLAM
FootSLAM
Inertial odometry
Eventually the position error will grow so large that the estimates become useless
-> (1) incorporating position measurements or map information
or (2) divide the navigation area into a grid of hexagons and then learn the probability of transitioning from one hexagon to an adjacent one
Notes: The problem with any odometry, though, is that eventually the position error will grow so large that the estimates become useless.
Now normally, we might seek to counteract this by incorporating position measurements or map information. But in this case, zero-velocity-aided inertial navigation is commonly seen as a navigation solution for unprepared and unexplored environments, and in these environments, we typically cannot assume that we have map information or any other direct information on absolute position.
What we can use, though, is an idea called FootSLAM, which is illustrated in the video to the left. The idea of FootSLAM is to divide the navigation area into a grid of hexagons and then learn the probability of transitioning from one hexagon to an adjacent one. In many practical situations, these probabilities will be stable over time and we can therefore obtain a navigation solution with a limited position error.

## Slide 33: Magneto-Inductive Navigation (heads-up, heavy maths ahead!)
Notes: Ok, so we’ve talked a lot about inertial navigation, but now let’s move onto another topic, namely magneto-inductive navigation, which is based on using the Earth’s magnetic field to work out where you are.

## Slide 34: Positioning with Magnetic Field
People have been using the Earth’s magnetic field for navigation since at least the 11th century A.D.
Animals too! They can sense the geomagnetic field (magnetoception)
Notes: So people have been using the Earth’s magnetic field for navigation since at least the 11th century A.D, when a Chinese scientist called Shen Kuo wrote about the existence of magnetic declination, which is the difference between magnetic north and true north. Magnetic compasses actually appeared in China as far back as the fourth century B.C., but they were originally used for feng shui rather than navigation. Meanwhile, in Europe, compasses were certainly being used for navigation by 1190 A.D., although it’s unclear whether or not the technology came from China or was developed separately.
Interestingly, though, many other organisms have been using the Earth’s magnetic field to navigate for much longer than we have, using an inbuilt ability to sense the field called magnetoception (also known as magnetoreception). And I guess one of the examples you’re most likely to have come across is that of a homing pigeon, but there are plenty of creatures that make use of magnetism, including hens, wood-mice, Zambian mole rats, and even some types of bacteria.

## Slide 35: Earth’s Magnetic Field
The intensity of the magnetic field varies from 0.25 Gauss at the Equator to 0.65 Gauss at the poles
Earth’s magnetic field can be well approximated by a magnetic dipole
Have we ever wondered why Earth has magnetic field?
Notes: So in practical terms, Earth’s magnetic field can be well approximated by a magnetic dipole, as you can see on this slide. And so in this diagram, m denotes the Earth’s magnetic moment, which is a vector pointing from the south pole to the north pole of the dipole, and B denotes the magnetic field. Note that the dipole isn’t perfectly aligned with the Earth’s axis in practice, so for example, magnetic north, the place towards which a compass will point, is not at the north pole, nor even in a fixed location on the Earth’s surface (it gradually moves around over time).
And the reason why Earth has a magnetic field is thought to boil down to electromagnetic induction caused by movements of liquid metals such as iron and nickel in the outer core. And this causes a current I, as shown in the slide, which in turn creates a magnetic field along the Earth’s axis.
Note that the intensity of the magnetic field is non-uniform, so at the Equator, it’s fairly weak, only measuring around 0.25 Gauss, whereas at the poles, it’s a lot stronger, at 0.65 Gauss.

## Slide 36: Why does Earth has magnetic field?

## Slide 37: Earth’s Magnetic Field
Notes: So as I mentioned on the previous slide, magnetic north and magnetic south are in general not at the north and south poles, so there’s a need to correct for that when navigating.
And to do this, we can use a magnetic declination chart such as the one in the slide, which basically captures the angle (on the horizontal plane) between magnetic north and true North. And this angle varies over the Earth’s surface and changes over time (note that magnetic north and south slowly move around).

## Slide 38: Earth’s Magnetic Field
The angle of the field alters over the surface of the Earth
Submarines in particular have exploited these microvariations to position themselves without suffering from Gyro drift
Accuracy is relatively coarse (kilometres)
Notes: The fact that the angle of the field alters over the Earth’s surface is actually quite useful, because this is something that can be exploited for positioning. And indeed, submarines in particular have exploited microvariations in the angle to position themselves without suffering from Gyro drift. However, it should be noted that the accuracy of this is relatively coarse (a matter of some kilometres). When that’s enough, it’s a useful technique, but some applications obviously require more precise positioning than that to function.

## Slide 39: Earth’s Magnetic Field
Indoors, ferromagnetic material, especially in reinforced concrete, distorts the Earth’s magnetic field.
Notes: Indoors, though, ferromagnetic material, especially in reinforced concrete, distorts the Earth’s magnetic field.

## Slide 40: Earth’s Magnetic Field
A spatial map of these distortions can be built, using techniques very similar to HORUS
The distortions themselves are not spatially unique
However, for someone moving through the area, the sequence of distortions can be exploited to provide positioning
Typical accuracy is around 2-3 m and various startups (IndoorAtlas) are exploiting this technique
Notes: And you can build a spatial map of these distortions, in a way that’s very similar to the Horus approach we mentioned previously.
In practice, these distortions aren’t spatially unique, but for someone moving through the area, it’s nevertheless possible to exploit the sequence of distortions to provide positioning.
And the accuracy of this is around 2-3m, which especially in large buildings is actually better than it sounds, and has led various startups, including IndoorAtlas, to exploit this technique.

## Slide 41: Earth’s Magnetic Field
Advantages:
  No infrastructure needs to be deployed
  Virtually all smart-phones have a magnetometer
  Adds absolute location to traditional IMU
Notes: And this technique clearly has advantages: it works without needing any additional infrastructure, since most smart-phones already have a magnetometer, and it’s capable of augmenting a traditional IMU with absolute location.

## Slide 42: Earth’s Magnetic Field
Disadvantages:
  Map has to be built and maintained
  Users can only be tracked when they move
  Accuracy is not good enough for many applications
Notes: But it does also have some downsides, especially that the map has to be built and maintained, and that users can only be tracked when they move. Moreover, whilst the 2-3m accuracy might be ok for some applications, it’s clearly nowhere near good enough for things like SLAM or augmented reality applications.

## Slide 43: Creating your own Magnetic Field
We can produce magnetic fields using coils of wire
  B ∝ INA
  I = current, N = number of turns, A = cross-sectional area
We can also sense a time-varying field using a coil of wire
  V ∝ B cos(θ)
Notes: So as an alternative to using the Earth’s magnetic field, we can of course also just make our own. And as some of you may remember from having seen electromagnetic induction in physics, this can be simply done by passing a current through a coil of wire. In terms of controlling the strength of the magnetic field that’s generated, it’s proportional to the strength of the current, the number of turns in the coil, and the cross-sectional area of the wire.
Note that a magnetic field that varies over time can also be sensed using a coil of wire, with the voltage you’ll measure being proportional to both the strength of the magnetic field and the angle theta between the magnetic field lines and the normal to the cross-sectional area of the coil.

## Slide 44: Modulation
Modulate the signal to make it easier to detect, especially compared with the strong Earth’s magnetic field
Notes: One additional thing to note in passing is that it’s also often helpful to modulate the electrical signal you use to create your magnetic field to make it easier to detect, especially in comparison to the strong magnetic field of the Earth.

## Slide 45: RSSI vs MI: Decay
|B| ∝ 1/r3
60 dB/decade
RSSI ∝ 1/r2
40 dB/decade
RSSI
MI
Magnetic fields fall off more rapidly
Notes: Ok, so how do magnetic fields compare to WiFi? Well, on the minus side, the signal strength decays much more rapidly than with WiFi. For WiFi, the falloff is quadratic with distance, whereas here it’s cubic.

## Slide 46: RSSI vs MI: Decay
|B| ∝ 1/r3
60 dB/decade
RSSI ∝ 1/r2
40 dB/decade
RSSI
MI
Magnetic fields fall off more rapidly
Range less than the traditional radio
Notes: And of course, in practice this means that the usable range is much less than with WiFi.

## Slide 47: RSSI vs MI: Antennas
RSSI
MI
Magnetic field controlled by size and shape of generating coil
Notes: But on the plus side, the magnetic field can be controlled by the size and shape of the generating coil, which is not possible with WiFi. And so here are a few examples of that.

## Slide 48: RSSI vs MI: Antennas
RSSI
MI
Magnetic field controlled by size and shape of generating coil

## Slide 49: RSSI vs MI: Antennas
RSSI
MI
Magnetic field controlled by size and shape of generating coil

## Slide 50: RSSI vs MI: Antennas
RSSI
MI
Magnetic field controlled by size and shape of generating coil

## Slide 51: RSSI vs MI: Antennas
RSSI
MI
Magnetic field controlled by size and shape of generating coil
Simple to alter field patterns to optimize localization
Notes: And this is clearly a nice thing to have in a localisation context, because it gives you a way of altering the field patterns to optimise your localisation performance.

## Slide 52: RSSI vs MI: Multipath and penetration
RSSI
MI
MI penetrates any non-metallic objects and does not suffer from multipath
Notes: Magnetic fields also have an advantage over WiFi in not suffering from multi-path effects, since they are able to penetrate any non-metallic objects.

## Slide 53: RSSI vs MI: Multipath and penetration
RSSI
MI
MI penetrates any non-metallic objects and does not suffer from multipath
Environmental obstacles do not affect MI localization accuracy
Notes: And this means that environmental obstacles don’t affect MI localization accuracy, which is clearly a big advantage.

## Slide 54: RSSI vs MI: Properties
MI is a vector field i.e. it has magnitude and direction
Using a triaxial sensor, we can make the device rotationally invariant
Notes: Another important point to note about MI fields is that they’re vector fields, in other words they have both a magnitude and a direction.
However, using a triaxial sensor, we can make our device rotationally invariant if desired.

## Slide 55: Magnetic Fields for Navigation
We can electronically control the orientation and the magnitude of the magnetic moment by using 3 mutually perpendicular coils
The sensor is also equipped with a triaxial coil
The total received power is invariant to TX and RX orientation
Distortion Rejecting Magneto-Inductive Three-Dimensional Localization (MagLoc) [Abrudan et al. 2015]
Notes: Ok, so now let’s talk more directly about how to use magnetic fields for navigation. And a lot of what I’m going to be talking about is based on a paper called MagLoc by Abrudan et al. from 2015.
So the basic setup here is that you have an MI transmitter and an MI receiver, each of which is triaxial, meaning that it has 3 mutually perpendicular coils, as shown in the slide. And then at the transmitter end, you can electronically control the orientation and the magnitude of the magnetic moment that gets transmitted using these coils. And at the receiver end, each of the three coils will have a different voltage induced in it, and you can use these values to figure out the relative pose of the receiver with respect to the transmitter.
One important thing to note is that the total received power is invariant to the relative orientation of the transmitter and receiver: that is, even though the voltages induced in the three receiver coils may vary with orientation, the overall power of the signal won’t change.

## Slide 56: Typical Measurements
The abrupt decay (60 dB/decade) of the magnetic field dB-magnitude corresponds to a path-loss exponent of 6 (i.e., 1 million time)
  Limits the transmission range 😢
  Enables easy detection of tiny changes in distance (few cm) 😊
Notes: Now as we saw earlier, the magnetic field decays at 60 dB/decade, which is quite abrupt, and for those of you who know a little bit about path loss, this corresponds to a path-loss exponent of 6. So on the one hand, that means that the transmission range is really quite limited, which is sad. But on the other hand, it does mean that we have an easy way of detecting tiny centimetre-scale changes in distance.

## Slide 57: Typical Measurements
Rx at 3m
Rx at 10 m
Rx at 20 m
Rx at 30 m
Notes: And so here we can see some examples of the received signals at different distances. And you can see that they’re nice and clear at short range, but the strength decreases and they get much noisier as the range increases.

## Slide 58: Maths behind MI
As previously mentioned we can:
  Generate and steer a magnetic vector using 3 orthogonal transmitting coils
  Sense and recover the magnetic vector using 3 orthogonal receiving coils
This provides the unique ability to localize a receiver using a single transmitter
Notes: So as previously mentioned, we can generate and steer a magnetic vector using a triaxial transmitter consisting of 3 orthogonal coils.
And we can also sense and recover that magnetic vector using a triaxial receiver likewise consisting of 3 orthogonal coils.
And what’s interesting about this is that it provides us with the unique ability to localize a receiver using a single transmitter, which is by no means the case for other modalities.

## Slide 59: Maths behind MI
With 3 transmitting antennas and 3 receiving antennas, we have a total of 9 measurements, of which 6 are unique
Using some physics we can work out the 6 degrees of freedom in the receiver (position and orientation)
Due to symmetry, we have a hemispherical ambiguity (receiver at (x,y,z) could also have been at (-x,-y,-z)), which can be solved with some prior knowledge (e.g., map information, IMU measurements).
Notes: So the reason for this is that by using a triaxial transmitter and a triaxial receiver, we have three transmitting coils and three receiving ones, which leads to a total of 9 measurements overall, of which 6 are unique. And if we use some physics, this gives us enough information to work out the 6 degrees of freedom of the receiver’s pose relative to the transmitter.
In practice, things are complicated a bit by the inherent symmetry of the magnetic field, meaning that a receiver at (x,y,z) could also have been at (-x,-y,-z). But this ambiguity can be removed using either a map, or inertial measurements or signals from two (or more) transmitters. And there’s more on that in the paper if you’re interested.

## Slide 60: Free-space Magnetic Channel Model
Consider TX located at the origin
Let RX position in 3D be described by the position vector
The range is
TX is energized in each axis, and the corresponding
  magnetic moments are:
= number of turn of the TX coil
= the coil input TX current
= the area of the TX coil
= 1, 2, 3 are the standard Euclidean basis vectors
Notes: Ok, so now let’s talk a bit about the magnetic channel model used in the MagLoc paper.
So starting simple, we’re going to assume that the transmitter’s placed at the origin, and that the receiver’s position is described by the position vector r = (xr, yr, zr), as shown in the slide. The range between the two is thus the L2 norm of r.
To transmit a signal, we energise the transmitter in each axis, which gives the magnetic moments shown on the slide. Each magnetic moment is in the direction of the basis vector for its axis, and has a magnitude equal to the product of the number of turns in the coil, the coil input current, and the area of the coil.

## Slide 61: Free-space Magnetic Channel Model
GOAL: Estimate the 3D position of RX
The B-field at an arbitrary position , given an arbitrary magnetic moment is:
= magnetic permeability of TX coil core
= 3x3 Identity matrix
= Matrix Transpose
For each TX magnetic moment ,, we get a vector
Notes: So now our goal is to estimate the 3D position of the receiver.
And to do this, we can start by thinking about the magnetic field at an arbitrary position r, given an arbitrary magnetic moment m, which is given by the equation shown in the slide. This is actually based on the magnetic dipole equations from Richard Feynman’s physics lectures, but for the purposes of this course, you can just take it as read.
The key point is that for each of the three magnetic moments mi transmitted, the magnetic field at the position of the receiver can be calculated as bi = B(r, mi), as shown in the slide. Note that each bi at this point will still be expressed in the transmitter’s frame.

## Slide 62: Free-space Magnetic Channel Model
Define the matrix whose columns are
Let be an orthogonal matrix describing the orientation of the RX frame w.r.t. the TX frame.
Then, the magnetic vector field described in the RX frame is
Notes: So now we can take these bi vectors, and make a matrix in which each column is one of the vectors, as shown in the slide.
And then if we pre-multiply this matrix by an orthogonal matrix describing the orientation of the receiver’s frame with respect to the transmitter’s frame, then we’ll get another matrix expressing the magnetic vector field in the receiver’s frame.

## Slide 63: Free-space Magnetic Channel Model
The voltages induced in the RX (x, y, z)-axes due to TX excitations are described by the following channel matrix
= frequency of the excitation
= number of turn of the RX coil
= magnetic permeability of the RX coil core
= the area of the RX coil
Notes: And so there will be voltages induced in the receiver’s x, y and z axes as a result of the excitation of the transmitter, which can be computed from the matrix we just computed, the frequency of the excitation and the parameters of the receiver’s coil as shown in the slide.
The physics details are not super important here, but what is important is that you end up with a 3x3 matrix called a channel matrix in which each element describes the voltage induced from one of the transmitter coils to one of the receiver ones.

## Slide 64: Free-space Magnetic Channel Model
Define the range-dependent scaling factor that also incorporates all the TX/RX coils specific constants
Then we can write
Note that the channel matrix depends on the position vector we are interested in, and on the orientation .
Notes: Now the full equation for the channel matrix S at this point would be a little long-winded, so in practice, we can define a range-dependent scaling factor c as shown in the slide that also incorporates all the specific constants associated with the transmitter and receiver coils, and then use it to simplify our definition of S.
So this actually ends up being quite a clean equation, and you can hopefully see that the channel matrix depends on both the position vector r we are interested in, i.e. the position of the receiver, and on the orientation omega. To put it another way, the channel matrix contains the position we’re after, and so if we can estimate the channel matrix at the receiver and work out a way of extracting the position from it, then we’re done.

## Slide 65: Free-space Magnetic Channel Model
The channel matrix containing the position information can be estimated at the RX using a known transmitted preamble
The input-output relationship of the 3 × 3 channel is
+ (Gaussian noise)
where and are the Nx3 transmitted and received preamble, respectively
Therefore, the LS estimate (which in this case is also Maximum Likelihood estimate) of the channel matrix is
- stands for the Moore-Penrose Pseudoinverse
Notes: So to estimate the channel matrix S at the receiver, we start by transmitting a known Nx3 sequence PTX from the transmitter. This will be received at the receiver as PRX, which is just PTX corrupted by some Gaussian noise. And the equation showing the relationship between PRX and PTX is shown in the slide, and clearly depends on the channel matrix S.
So we can use this to estimate S by using the least-squares approach shown in the slide, which it turns out also yields a maximum likelihood estimate of S.

## Slide 66: Free-space Magnetic Channel Model
Let us analyze a bit the channel matrix and try to infer the range
The scaling factor and therefore contains the range information
The latter factor depends only on the versor (i.e., only on the direction of the position vector, not on its magnitude).
Therefore, in free-space, the Frobenius norm of also decays with the cube of the range, and can be used for range estimation.
Since orthogonal matrices preserve the Frobenius norm, the range estimate is invariant w.r.t. TX/RX relative orientation
Notes: Ok, so given S, we now want to try to extract the position vector. And to do that, we start by inferring its range r.
So let’s look again at our equation for S, and recall that c, our range-dependent scaling factor whose definition we saw a couple of slides back, is proportional to 1/r3. By contrast, note that the second factor in the equation for S is range-independent, since it depends only on the direction of the position vector, not on its magnitude. So in free-space, the Frobenius norm of S is also proportional to 1/r3, and we can use this for range estimation.
Incidentally, note that since orthogonal matrices like omega preserve the Frobenius norm, the range estimate is invariant with regard to the relative orientation between the transmitter and the receiver.

## Slide 67: Free-space Magnetic Channel Model
Define the overall RSSI (Received Signal Strength Indicator) measured in dB as
Since , the law describing the RSSI vs. distance in free-space is
  (This is why we have the propagation loss of 60db/decade)
where is the RSSI measured at some reference distance
Therefore, the range estimate in free-space is
When plotting the RSSI vs. the log-distance , the slope of the line is 60dB/decade
Notes: So to start with, we can define the overall RSSI measured in decibels as .
Now since the Frobenius norm of S is proportional to 1/r3, the equation that relates the RSSI to the distance in free-space is , where is the RSSI measured at some reference distance .
And we can thus calculate the range estimate in free-space as , as shown in the slide.
Note that when plotting the RSSI vs. the log-distance , the slope of the line is 60dB/decade.
So to start with, we can define the overall RSSI measured in decibels as 𝜌=20𝑙𝑜𝑔‖𝑆‖_𝐹.
Now since the Frobenius norm of S is proportional to 1/r3, the equation that relates the RSSI to the distance in free-space is 𝜌=𝜌_0 −60log (𝑟/𝑟_0 ), where 𝜌_0 is the RSSI measured at some reference distance 𝑟_0.
And we can thus calculate the range estimate in free-space as 𝑟=𝑟_0 10^((𝜌_0 "−" 𝜌)/60), as shown in the slide.
Note that when plotting the RSSI vs. the log-distance log (𝑟/𝑟_0 ), the slope of the line is 60dB/decade.

## Slide 68: Free-space Magnetic Channel Model
Our next goal is to determine the position vector
Its modulus (range) is known by now, we only need to determine its direction in 3D. Recall that
We first get rid of the arbitrary RX orientation as follows
Define the channel inner product
From previous equations we have
* Since is orthogonal
Notes: So now that we have the range estimate, our next goal is to determine the position vector. And given that we already have its norm, we now only actually need to determine its direction in 3D.
So returning to our definition of S, the first step is to get rid of the arbitrary receiver orientation omega, which we can do by computing the channel Gram matrix as shown in the slide. So the key thing to note here is that since omega is orthogonal, its transpose will be equal to its inverse, and so will simply equal the identity and get cancelled out. And so C will then be independent of omega.
So now that we have the range estimate, our next goal is to determine the position vector. And given that we already have its norm, we now only actually need to determine its direction in 3D.
So returning to our definition of S, the first step is to get rid of the arbitrary receiver orientation omega, which we can do by computing the channel Gram matrix 𝐶=𝑆^𝑇 𝑆 as shown in the slide. So the key thing to note here is that since omega is orthogonal, its transpose will be equal to its inverse, and so Ω^𝑇 Ω will simply equal the identity and get cancelled out. And so C will then be independent of omega.

## Slide 69: Free-space Magnetic Channel Model
Let be the eigen-decomposition of the channel inner product . We get
* and
Which is a rank-one matrix
Consequently, the maximal eigenvector of is the position versor
we are interested in:
Finally, the 3D position is given by
Notes: Ok, so now let’s consider the eigen-decomposition of C, namely .
Now from the definition of C on the previous slide, we can see that .
And so since and, we get that that also equals , as shown in the slide. And this is clearly a rank-one matrix, since it equals the outer product of a row vector and a column vector.
As a consequence of this, the maximal eigenvector umax of C ends up being the position versor we’re interested in, in other words the normalised version of the position vector. And so given that and the range we previously estimated, we can estimate the final 3D position as shown in the slide.
Ok, so now let’s consider the eigen-decomposition of C, namely 𝑈𝐷𝑈^𝑇.
Now from the definition of C on the previous slide, we can see that r/‖r‖ r^𝑇/‖r‖ = 1/3𝑐 C^(1/2)+1/3 𝐼_3.
And so since C^(1/2)=𝑈D^(1/2) 𝑈^𝑇and𝐼_3=𝑈𝑈^𝑇, we get that that also equals 𝑈[1/3𝑐 𝐷^(1/2) +1/3 I_3 ] 𝑈^𝑇, as shown in the slide. And this is clearly a rank-one matrix, since it equals the outer product of a row vector and a column vector.
As a consequence of this, the maximal eigenvector umax of C ends up being the position versor we’re interested in, in other words the normalised version of the position vector. And so given that and the range we previously estimated, we can estimate the final 3D position as shown in the slide.

## Slide 70: Summary
If some property varies over space, then there is a strong chance that someone has or will use it for positioning!
Magneto-Inductive positioning has some unique properties which make it an interesting alternative
Positioning itself though is just another sensor - it is what we do with it that is important
Notes: Ok, so to conclude the lecture then, if there’s some property that varies over space, then there’s a strong chance that someone either has used it, or at some point will use it, for positioning.
And one example of that is the magneto-inductive positioning we just saw, which has some unique properties that make it an interesting option.
However, in the end, positioning itself is effectively just another sensor – it’s what we do with it that’s important.